LEVANOLA OIL

Manufacturer:

TARSIS LTD P.O. BOX 2630 PETHACH TIKVA 4912502

TEL:	972-3-9223785

FAX:	972-3-9243618

Updated:05/2020

- PRODUCT AND COMPANY IDENTIFICATION

Product  name:	 Levanola Oil

Product Type:	Agricultural Summer Oil

Supplier:	TARSIS LTD P.O. BOX 10156 PETHACH TIKVA						Tel	972-3-9223785

Emergency Telephone Number:  Mr. Shevach Tenzer , tel. 972-52-3893739

- HAZARD IDENTIFICATION

Hazard Statements

H302 - Harmful if swallowed

H304 - May be fatal  if swallowed and enters airways

H317 – Prolonged skin contact may cause dermatitis

Precautionary Statements

P261 – Avoid breathing mists, vapours or spray

P280 – Wear protective gloves, clothing eye and face protection

P301+P330 – If swallowed immediately call a physician or a poison

information center

P331 – If swallowed : do not induce vomiting

P501- Dispose of container or waste as hazardous meterial

P270 – Do not eat , drink or smoke when using this product.

P271 – Use only outdoor or in a well-ventilated area

P363 – Wash contaminated clothing before reuse

P304+P340 – If vapors inhaled : take victim to fresh air and keep him at rest in a comfortable breathing position.

- COMPOSITION and INFORMATION on INGREDIENTS

| Ingredient Name | CAS reg. no. | (Range) % w/w |
| --- | --- | --- |
| Solvent refined light paraffinic oil | 64741-89-5 | 78 – 82% |
| Other ingredients |  | 18 – 22% |

- FIRST AID MEASURES

Never give fluids or induce vomiting if patient is unconscious or is having convulsions.

INGESTION:

Keep patient at rest. Do not induce vomiting .

EYE CONTACT:

Hold eyelids open and wash eyes with plenty of water for at least 15 minutes. Seek medical advice immediately and show product label to the physician.

SKIN CONTACT:

Remove contaminated clothing and  wash skin with soap and plenty of water. If irritation persists obtain medical advice

INHALATHION:

Inhalation of vapors is normally not a problem. If over exposed to oil mist remove the victim immediately to fresh air. Obtain medical advice

- FIRE FIGHTING  MEASURES

FIRE  EXTINGUISHING MEDIA:

Carbon dioxide. Dry chemical powder or foam.

EXTINGUISHING MEDIA HAZARDS:

If involved in a fire , carbon monoxide may be formed in the event of incomplete combustion

PROTECTION OF  FIRE FIGHTING:

Wear  protective clothing and eye protection, and use self contained breathing apparatus.

- ACCIDENTAL RELEASE MEASURES

PERSONAL PRECAUTIONS:

Avoid contact with skin and eyes. Avoid breathing vapors or mist

Wear protective clothing and eye protection. Remove contaminated clothing , wash skin area with soap and water and  launder clothing before reuse or dispose of properly.

PRECAUSIONS FOR THE ENVIRONMENT:

Do not wash into sewers or into any body of water. Discharge into the environment must be avioded.

CLEANUP METHODS:

Small spillage: absorb on inert absorbing material such as sand or clay. Shovel up into covered containers for disposal. Large spillage: Should be dammed-off and pumped into containers: soak up reminder with absorbent material and dispose of in accordance with local regulations.

- HANDLING AND STORAGE

HANDLING:

Good personal hygiene procedures must be practiced. Do not consume or store food  in the work area.

Before eating, drinking or smoking and after work, wash hands and exposed skin using liquid detergent

STORAGE:

Place in a locked  cool, dry and ventilated areas, store only in closed, properly-labeled containers, in area

designed specifically for pesticides. Keep out of the reach of children and unauthorized persons. Properly keep away from food, drink and animal feeding stuffs.

Do not store with seeds, fertilizers or foodstuffs.

Protect from direct sunlight and refrain from temperatures above 400C.

Containers which are opened or damaged must be carefully resealed and kept upright to prevent leakage

- EXPOSURE CONTROLS AND PERSONAL PROTECTION

PERSONAL PROTECTIVE EQUIPMENT:

RESPIRATORY PROTECTION:

Use a full-face respirator with ABEK (EN-14387) respirator cartridges

HAND & SKIN PROTECTION:

Wear protective clothing: long sleeved shirts and pants, hat , rubber boots with socks,  protective goggles and chemical  resistant impermeable gloves should be needed like neoprene.

EYE/FACE PROTECTION:

Wear  protective goggles

GENERAL PRECAUTIONS:

Avoid prolonged and repeated contact with eyes and the skin

Clothing must be laundered after each day’s use.

- PHYSICAL AND CHEMICAL PROPERTIES

Appearance:	 	White mayonnaise with mild ammonical odor.

Ph				6-8

Specific gravity:		 0.856 +/- 0.005 (200 C)

Kinematic Viscosity:	NA

Flash point 			>1200

Solubility (at 250C)		Emulsifiable

- STABILITY AND REACTIVITY

REACTIVITY:  No data available

STABILITY: Stable at conventional temperatures for storage, handling & use

INCOMPATIBLE MATERIALS: Strong alkaline & acidic compounds or oxidising compounds .

HAZARDOUS DECOMPOSITION PRODUCTS: Incomplete combustion produces gases such as CO & CO2. Various forms of hydrocarbons, aldehydes etc. Product does not decompose at normal handling temperatures.

- TOXICOLOGICAL INFORMATION

ACUTE TOXICITY

ACUTE ORAL:		LD50 for  rats >5000 mg/kg body weight

EYE IRRITATION:             Moderately irritant

Inhalation:		negligible at ambient temperatures. Elevated temperatures may form vapors, mists or fumes which may be irritating to the eyes, nose, throat & lungs.

ACUTE DERMAL:	LD50 for  rabbit  > 2000 mg/kg

SKIN IRRITATION:	slightly irritant

SKIN Sensitization: for guinea pig – not a sensitizer

Specific effects – No carcinogenic effects in laboratory animals

- ECOLOGICAL INFORMATION

ECOTOXICITY – when spilled to water bodies it forms a film on water surface, thus can be toxic to fish, daphnia & algae.

When released to soil will remain on the soil surface. Not harmfull to terrestrial animals

Not inhibitory to sewage bacteria

Bioaccumulation: Bioaccumulative based on logP values of constiuents.

- DISPOSAL COSIDERATION

Do not contaminate ponds, waterways or ditches with chemical or used container.

The preferred option is to send to local licensed disposals.

Any disposal practice must be in compliance with all local and national  laws and regulations.

- TRANSPORT INFORMATION

Usual shipping containers: rail cars, tankn trucks, drums.

TRANSPORT HAZARD CLASS  - 3

UN NUMBER – None

Transport. temperatures – ambient to 600

- REGULATORY INFORMATION

This product is registered under the PPIS registration:

Registration No. 303/ppis/1972

Approved users of this product are people who have been instructed with the product propetues and risks, are familiar with the product label and behave accordingly.

Israeli regulations – Hazardous Substances Law, 1993; Hazrdous Substances Regulations (Import & Export of Hazrdous Wastes), 1994; Licensing of Business Regulations (Oil Storage), 1976; Licensing of Businesses Regulations (Disposal of Hazrdous Wastes) 1990,; Plant Protection Act 1994

- OTHER INFORMATION

The information provided in this safety data sheet is correct to the best knowledge, information and belief at the data of its publication. The information given is designed only as a guidance for safe handling, use, processing, storage, transportation, disposal and release and is not to be considered as a warranty or quality specification.

The information relates only to the specific material designated and may not be valid for such material used in combination with other materials.

This data belongs to TARSIS LTD. All Rights reserved