# MATERIAL SAFETY DATA SHEET

# DINO SUPER 15  EC

Manufacturer: 	TARSIS LTD P.O. BOX 10156 PETHACH TIKVA						TEL:	972-3-9223785

FAX:	972-3-9243618 					Update:6/2012

===========================================================================

- PRODUCT IDENTIFICATION

===========================================================================

Product  name:	 Dino Super 15 EC

Application:	Agricultural oil

Supplier:	TARSIS LTD P.O. BOX 10156 PETHACH TIKVA						Tel	972-3-9223785

==========================================================================

2.  COMPOSITION/INFORMATION ON INGREDIENTS

===========================================================================

MATERIAL			 CAS			RANGE(W/V)

Dinocap II (Meptyldinocap)	131-72-6		15G/L

Sunspray oil			64741-89-5		709 G/L

Solvent+emulsifires

===========================================================================

- HAZARD IDENTIFICATION

===========================================================================

Flammable.  May cause sensitization and  irritation by skin contact.  Risk of serious damage to eyes.

Very toxic to aquatic organisms. May cause long term adverse effects in the aquatic environments.

Avoid contact with skin,eyes and clothing.

===========================================================================

- FIRST AID MEASURES

========================================================

===================

Never give fluids or induce vomiting if patient is unconscious or is having convulsions.

INGESTION:

Do not induce vomiting or give liquids. Do not give water.  Call a physician . The decision of whether to induce vomiting or not should be made by a physician.

EYE CONTACT:

Plush eyes with plenty of water for at least 15 minutes. Consult a physician if irritation persists.

SKIN CONTACT:

Remove contaminated clothing and  wash skin with soap and plenty of water. Consult a physician. Wash contaminated clothing before reuse.

INHALATHION:

Remove the victim immediately to fresh air. Consult a physician.

Note to Physician:

Supportive care. Treatment based on judgement of physician in response to symptoms of patient. Measures against circulatory shock, respiratory depressin and convulsions may be needed.

===========================================================================

5.  FIRE-FIGHTING MEASURES

===========================================================================

FIRE  EXTINGUISHING MEDIA:

Carbon dioxide. Dry chemical. Foam. Avoid high water jet, use water jet only to cool down surfaces exposed to fire.

HAZARDOOUS DECOMPOSITION PRODUCT:

During a fire, smoke may contain the original material in addition to unidentified toxic and or irritating compounds.

Combustion products include  Nitrogen oxides, oxides of carbon, compounds of sulphur, chlorine and productsof incomplete combustion.

PROTECTION OF  FIRE FIGHTING:

Wear protective clothing and eye protection, and use self contained breathing apparatus.

===========================================================================

6.  ACCIDENTAL RELEASE MEASURES

===========================================================================

PERSONAL PRECAUTIONS:

Avoid contact with skin and eyes.

Wear protective clothing and eye protection. Remove contaminated clothing immediately, wash skin area with soap and water and  launder clothing before reuse or dispose of properly.

PRECAUSIONS FOR THE ENVIRONMENT:

Do not wash into sewers or into any body of water. Advise water authority if spillage has entered water course or drainage system.

CLEANUP METHODS:

Small spillage: absorb on inert absorbing material such as sand or clay. Shovel up into covered containers for disposal. Large spillage: Should be dammed-off and pumped into containers: soak up reminder with absorbent material and dispose of in accordance with local regulations.

===========================================================================

7.  HANDLING AND STORAGE

===========================================================================

HANDLING:

A sufficient ventilation must guarantee an exposure which do not exceed the acceptable limit.

Good personal hygiene procedures must be practiced. Do not consume or store food  in the work area.

Before eating, drinking or smoking and after work, wash hands and exposed skin using liquid detergent

STORAGE:

Place in cool, dry and ventilated areas, store only in closed, properly-labeled containers, in area

designed specifically for pesticides. Keep out of the reach of children and unauthorized persons. Keep

away from excessive heat and open flame. Properly keep away from food, drink and animal feeding stuffs.

==========================================================================

8.  EXPOSURE CONTROL/PERSONAL PROTECTION

===========================================================================

PERSONAL PROTECTION:

RESPIRATORY PROTECTION:

For most conditions no respiratory protection should be needed.

However, when airborne exposure guidelines and or comfort levels may be exceeded use an approved air purifying respirator.

For emergency conditions, use an approved positive-pressure self contained breathing apparatus.

HAND & SKIN PROTECTION:

For brief contact, no precautios other than clean body-covering clothing and chemical  resistant gloves should be needed like neoprene. When prolonged or frequently repeated contact could occur, use protective clothing impervious to this material.

For emergency conditions: use protective clothing impervious to this  material. Selection of specific items will depend on operation.

EYE/FACE PROTECTION:

Wear protective goggles and face shield.

GENERAL PRECAUTIONS:

Clothing must be laundered after each day’s use.

EXPOSURE LIMITS VALUE:

SUSPRAY 6N:

The recommended exposure limits (ACGIH) of oil mists TLV/TWA (8h) 5 mg/m3

The recommended exposure limits (ACGIH) of oil mists TLV/STEL 10 mg/m3

ISOBUTYL ALCOHOL: 50ppm (ACGIH)

Danger: Irritates the skin. Dangerous if ingested. Extremly irritating to the eyes.

===========================================================================

9. PHYSICAL AND CHEMICAL PROPETIES

===========================================================================

Appearance/odour:	 	Amber, petroleum hydrocarbon odour, liquid.

Density:				0.85 g/ml

Solubility in water 		Emulsifies with water

===========================================================================

===========================================================================

10.  STABILITY AND REACTIVITY

===========================================================================

CONDITION TO AVOID:

Keep away from heat sources, open flames and other sources of ignition.

MATERIALS TO AVOID:

Avoid contact with strong oxidants such as liquid chlorine and concentrated oxygen, acids, bases, amines, iron, halogen.

HAZARDOUS DECOMPOSITION PRODUCTS:

Incomplete burning can cause formation of dangerous gasses like CO, CO2, compoundes of sulphur, and nitrogen.

===========================================================================

11. TOXICOLOGICAL DATA

===========================================================================

ACUTE TOXICITY

INGESTION  		Low toxicity if swallowed, the oral LD50 for rats is>2000 mg/kg

SKIN CONTACT	May cause skin irritation, the dermal  LD50 for rats is>2000 mg/kg

EYE CONTACT 	May cause eye irritation. Risk of serious damage to eyes

Sensitization:	Skin contact can cause sensitization /an allergic skin reaction

Inhalation 	Inhalation of  mist and vapours generated at elevated temperatures  may cause  respiratory irritation.

===========================================================================

12.  ECOLOGICAL INFORMATION

===========================================================================

ECOTOXICITY: Very toxic to fish on an cute basic(LC 50<1mg/l),

Very toxic to aquatic inverterbrate on an cute basic(EC 50<1mg/l),

Very toxic to algae on an cute basic(LC 50<1mg/l),

May cause long term adverse effects in the aquatic environments

PERSISTENCE and DEGRADABILITY: Not readily biodegradable

===========================================================================

13.  DISPOSAL CONSIDERATIONS

===========================================================================

Do not contaminate ponds, waterways or ditches with chemical or used container.

The preferred option is to send to local licensed disposals.

Any disposal practice must be in compliance with all local and national  laws and regulations.

========================================================

===================

14.  TRANSPORT INFORMATIONS

===========================================================================

SPECIAL PRECAUTIONS:

Hazrd class: 3 Flamaable

Packing group: III

Environmentally Hazardous Substance

Stable at room temperature and during transport.

Transport by road, rail sea and air, in properly sealed and labeled containers.

U.N. NUMBER:  1212

========================================================

===================

15.  REGULATORY INFORMATION

===========================================================================

Hazard Symbol:		Flammable , Irritant, Dangerous for the environment

Risk Pharases:

R38: Irritating to skin

R41: Risk of serious damage to eyes

R43: May cause sensitization by skin contact.

R50/R53: Very toxic to aquatic organisms/ May cause long term adverse effects in the aquatic environments

Safety Pharases: 	S 2: Keep locked up and out of reach of children

S 37: Wear suitable protective gloves

S 60: This material and its container must be disposed of

as hazardous waste

S 61: Avoid release to the environment. Refer to special instruction/safety data sheet

===========================================================================

16. OTHER INFORMATION

===========================================================================

The information provided in this safety data sheet is correct to the best knowledge, information and belief at the data of its publication. The information given is designed only as a guidance for safe handling, use, processing, storage, transportation, disposal and release and is not to be considered as a warranty or quality specification.

The information relates only to the specific material designated and may not be valid for such material used in combination with other materials.

This data belongs to TARSIS LTD. All Rights reserved